## Slide 1: Cross Band Transponder (XBT) or Multi-Channel FM Transponder
Andrew Robinson
KA3WDW
30Apr2024
Special Acknowledgement: Dr. Joseph DiVerdi

## Slide 2: Review Objectives
Share current progress on concept
Engage community to gather comments, use cases, ideas, thoughts, opinions, etc.
Solicit help to continue this work

## Slide 3: High Level Needs (from Jonathan’s email)
Start with:
  Single signal path
  VHF voice signal transponded as a UHF voice signal
Could be a SDR w/digital radio chip
Could be analog
Fit onto a CubeSat board
  Ideally 2” x 2” area
Radiation tolerant
  Avoid CMOS

## Slide 4: Goals
Multiple transponders on a single satellite
  I.e., multiple up frequencies with multiple down frequencies
Low SWaP-C
Other desired capabilities?
  Brainstorm session to build a “wish list”

## Slide 5: Concept of Operations (CONOPS)

## Slide 6: OV-1
fVHF,1
fVHF,2
fVHF,N
fUHF,1
fUHF,2
fUHF,N
Multiple (how many?) transponders on a single satellite
  Up in VHF
  Down in UHF

## Slide 7: CONOPS
Main mission:
  Receive TBD number of VHF signals from aperture
  Amplify/filter/condition incoming signals for processing
  Process signals
  Filter/condition/amplify outgoing signal
  Transmit UHF signals to aperture
Other Use Cases:
  SOH, failure recovery
  Store and forward?
  Software updates
  Different/new/etc. modes

## Slide 8: Architecture

## Slide 9: High-Level Block Diagram
Down
Converter
ADC
Signal
Processor
DAC
Up
Converter
144-146 MHz
LNA
PA
420-450 MHz
System of Interest

## Slide 10: Context Diagram
Cross Band Transponder
Host Bus
Power
Commands
TLM
Apertures
Tx Signals
Rx Signals
Will the Bus have a comm system for TLM D/L or will the XBT be used?

## Slide 11
Cross Band Transponder
Power
TLM
Processor
Tx
Signals
Rx
Signals
Rx Front End
PA
Tx Front End
ADC
Digital Down-converter
Digital Up-converter
DAC
DC/DC
To Components
Commands
Reference signal: needed? (probably)  internal or external?
RFIC

## Slide 12: RFIC
Functionality needed:
  Analog receive
  Amplify
  Mix with LO to IF
  ADC
  DAC
  Mix with LO to RF
  Analog transmit
Baseline: Analog Devices AD9361
  12-bit DAC and ADC’s
  TX: 47 MHz to 6.0 GHz, RX: 70 MHz to 6.0 GHz
  Other options?
From AD9361 Data Sheet

## Slide 13: Processor
Functionality needed:
  Demodulate signal
  Shift signal
  What else..??
Notes/Questions/Observations:

## Slide 14: Processor Exploration – scratch the ASCENT itch
Prompted a variety of LLM’s to brainstorm low power processor options:
  TI Tiva C Series
  STMicroelectronics STM32F7 Series
  Microchip Technology PIC32MX Series
  NXP Semiconductors i.MX6 Series
  Espressif Systems ESP32/ESP8266
  TI TMS320C6000 Series  see follow-on slide
  Xilinx Zynq UltraScale+ MPSoC
  Analog Devices ADSP-SC58x/ADSP-2158x
  Microchip dsPIC33CH
  Renesas R-Car V3H

## Slide 15: Processor Option (1 of n)
TI TMS320C6000 Series
  High performance DSP w/low power
  Very Long Instruction Word (VLIW)  efficient parallel processing
  E.g., TMS320C6455BCTZA
    -40C to 90C
    1 GHz clock rate
    $291.15 and 43 in stock (DigiKey)
  Evaluation board: TMDXEV6455
    $1,895.52 and 1 in stock (DigiKey)
  Radiation-hardened version available  SMJ320C6701-SP

## Slide 16: Processor Option (2 of n)
WIP

## Slide 17: Power Amplifier (PA)
Functions  Form:
Amplify the RF signal
Notes/Questions/Observations:
What power is required to close the link?
  Frequency, aperture, altitude dependent?

## Slide 18: Other Potential Components to Explore
ADRV904x Block Diagram

## Slide 19: Prototyping

## Slide 20: Early Prototyping Ideas
Potential Options:
  Radioberry w/Raspbery Pi (and required converters)
  LimeSDR
  Others?
Purpose: Exploration on non-flight COTS parts to gain confidence/experience while going through conceptual design

## Slide 21: Acronyms
Acronym | Definition
ADC | Analog to Digital Conversion
COTS | Commercial Off The Shelf
D/L | Downlink
DAC | Digital to Analog Conversion
DC | Direct Current
FM | Frequency Modulation
IF | Intermediate Frequency
LNA | Low Noise Amplifier
LO | Local Oscillator
PA | Power Amplifier
RF | Radio Frequency
RFIC | Radio Frequency Integrated Circuit
Rx | Receive
SDR | Software Defined Radio
TLM | Telemetry
Tx | Transmit
U/L | Uplink
XBT | Cross Band Transponder

## Slide 22: Backup

## Slide 23: Assumptions
# | Title | Assumption
1 | Input Power | A single source of power will be received from the bus Conversion and distribution of power is a function of the XBT
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 

## Slide 24: High-Level Questions
# | Question | Response
1 | Are there any desired additional capabilities that we can enhance with a digital design or a SDR design? | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 

## Slide 25: Requirements(-ish)

## Slide 26: Design-y Questions
# | Question | Response
1 | What TLM is typically collected? | 
2 | How many signals? | 
3 | What is a good power draw to shoot for? | 
4 | Are reference signals (e.g., PPS, 50 MHz) available from the bus or should they be accounted for on the XBT? | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 

## Slide 27: SDR
Fairwaves
XTRX
Source: https://www.crowdsupply.com/fairwaves/xtrx

## Slide 28: SDR
Lime Microsystems took over the XTRX (?)
Additional Options:
Source: https://limemicro.com/products/boards/

## Slide 29: SDR
AntSDR E200